## Slide 1: Hybrid Networking Model in a holistic setup using Cisco Packet Tracer

## Slide 2: Tools and Concepts
CISCO PACKET TRACER
Virtual LAN
Inter-VLAN
OSPF – Open Shortest Path First
Security
Access Control List
Network Address Translator
Dynamic Host Configuration Protocol

## Slide 3: Cisco Packet Tracer Simulation, Visualization, Collaboration
Simulate IOS Commands
01
Visualize Network Traffic
02
Collaborate on Multiuser Activities
03

## Slide 4: Cisco Packet Tracer
Logical and Physical Workspaces
Real-Time and Simulation Modes
User friendly Command Line Interface (CLI)
Global event list (packet sniffer)
LAN, switching, TCP/IP, routing, and WAN protocols
Activity Wizard, Lab grading
Multiuser functionality
Multiple platform support
Multiple language support
Integrated Help and Tutorials

## Slide 5: Creating a Network for College
Local Area Network
Use of Routers & Switches
Virtual LAN in Switches: Large broadcast domain to small broadcast domain

## Slide 6: Open Shortest Path First Routing Protocol
Routing : moving packet from one network to another
OSPF – Link State Routing Protocol
Classless Routing Protocol
‘Dijkstra's algorithm
Autonomous System number and Area
Area 0 : backbone area (Range 0-65535)
Uses Wildcard (Reverse subnet)
No limit on hops
Administrative Distance is 110

## Slide 7: Virtual Local Area Network
Logical Function – enhances network security
Implemented in Manageable Switches (Multicast Collision Domain-Layer 2 devices)
Learns Address  Filters Decision  Avoids Loop  Converts Large broadcast domain to smaller segments

## Slide 8: Inter-VLAN Routing
Using dot1q protocol : can be implemented on components of different vendors
We logically divide router’s interface fa 0/0 to sub-interfaces fa 0/0.1, fa 0/0.2 etc.
We assign fa 0/0.1 an IP of VLAN1 , fa 0/0.2 an IP of VLAN2 and so on.
We configure switchport as trunk port and connect it to router’s interface.
VLAN1 should have gateway IP with respect to fa 0/0.1
Configure router

## Slide 9: Security
Software Security
Configuring Passwords
Enable : to enter privileged mode
Secret : stored in router’s configuration in an encrypted form
Console : authenticate router through console port
Telnet : Line VTY , authenticate router through telnet

## Slide 10: Network Address Translator
Translates private(source) IP address while sending it through Layer 3 device
From local IP to internet IP address
Private IP addresses :
10.0.0.0 - 10.255.255.255
172.16.0.0 -172.31.255.255
192.168.0.0 - 192.168.255.255
Static NAT : mapping IP one to one.
Dynamic NAT : assign range & automatically translate different IP to hosts.

## Slide 11: Dynamic Host Configuration Protocol
Provides IP address on client side dynamically
Configure NIC Settings – IP address, Subnet mask, Default Gateway IP, DNS Server IP
Automatic configuration
DORA Process
Discover
Offer
Request
Acknowledge

## Slide 12: Thank You